Keypad overview:

Main function:

Keys:				Function:

0 1 2 3 4 5 6 7 8 9 		Enter channel, frequency of number

*				Scan

#				Reverse shift

TS	(A)			Activate tone squelch (ZVEI)

C	(B)			Go to callchannel

M/V	(C)			Change VFO and memory

F	(D)			Function key, activates second function of next key.

Second function:

Keys:				Function:

1				Transmitter power

2				Squelch level

4				MENU

5				Status menu

*				Skip memory channel when scanning

#				Shift + / - / none

TS	(A)			Enter tone-squelch code

C	(B)			Delete call channel

M/V	(C)			Delete memory channel

These are the settings of the menu, the values are changable by entering the F key.

- Shift								(       ****** kHz

This is the shift, default 1.6MHz

- Range							Fr              4344 /

VCO range 4344 = 430-440, 3049 = 300-500		                  3049

- Scan mode							SC    Wait until end/

Action when a signal is detected while scanning 		         Wait short      /

scannen.							         Stop scan

- Scan mode							SC    Carrier           /

Squelch

- Beep								tP      On /

Keypad beep						         Off

- Rogerbeep							rP      On /

Off

- ZVEI tones							5t                         ***

This is the length of the ZVEI tones.

- LCD light							LC                       ***

The burn time of the LCD light after pressing a key.

- Settings							IN	SAVE

The start-up situation can be changed here. Configure

the porto and press the F key at this menu item.

- Frequency							Fr	SAVE

This is the start-up frequency. When pressing the F

key here, the porto starts at the selected frequency